How to load multiple files to buffer and edit the data in buffer

SuperPro programmer software provides the powerful data loading and buffer editing functions for all types of devices. They help to load the files to the chip memory and program the device correctly.

1. Load multiple files to the device memory

- Click “Buffer” and disable “Buffer clear on data load” in buffer edit window (Figure 1). Then load multiple files in sequence.

Figure 1

- Select Load from the File menu to open the Load File dialog box (Figure 2).             Select the file type from the Files of type drop down list.

Figure 2

- The user can define Buffer address and File address shown in Load File screen (Figure 3).

Buffer Address field displays the start address of the loaded data in buffer.

File address field displays the start address the file you want to load to buffer.

Figure 3

The user can save the buffer data and make a new combined file by clicking “Save”.

2. Edit data in Buffer

Figure 1 shows different functions for editing data in buffer, such as Locate, Fill, Search, Swap, etc.

- Locate

Locate function allows the user to quickly display the data in the certain memory address.

Figure 4

- Fill

This function consists of the Fill Start Address, End Address, Fill Data input lines.

For example, you use it to empty the data in buffer.

Figure 5

- Swap

This function is use to Swap MSB and LSB byte order for the specified word width in the address range.

Figure 6

4) Radix

Radix function is used to Toggle between HEX and DEC memory address display.