# Operating from ATE port

ATE control port is used for communication with external host or integration into the automatic programming and test equipment. Therefore, besides the keyboard, the user can also operate ISP programmer through ATE interface. ATE equipment interface adopts opto-coupling device to isolate signals, in order to ensure security and accuracy of signals between the two equipments. In addition, while using ATE interface, it is required to set the power voltage of external equipment signal and appropriate reference voltage point correctly. The physical map of ATE is as follows:

For the signals of ATE port, please refer to the diagram below:

Description of signals:

OPTO_VCC: Working power of ATE controlling port is supplied by exterior controlling equipment and it should match signal voltage. Voltage difference between both OPTO_VCC and OPTO_GND1 or OPTO_GND2 should be no more than 24V. Normally, the value is between 5V - 24V.

SEL0-SEL5: These input signals are used to select project. The Available working voltage range of SEL signals should be consistent with OPTO_VCC.

START, RESET: These are Input signals and the available working voltage range should be consistent with OPTO_VCC. For detailed instruction, please refer to “ATE Instruction”.

PASS, FAIL: These are output signals and the available working voltage range is between OPTO_GND2 and OPTO_VCC-0.8V. For detailed instruction, please refer to “ATE Instruction”.

OPTO_GND1: Exterior controlling equipment GND1, which is used to input signals of SEL0-SEL5, STAET and RESET.

OPTO_GND2：Exterior controlling equipment GND2, which is used to output signals of PASS and FAIL.

VCC：IS01 supplies 3.3V output

GND：IS01 supplies GND output

TIPS:

- If input and output signals from exterior controlling equipment have common ground, OPTO_GND1 and OPTO_GND2 should be the same.

2. When exterior controlling voltage OPTO_VCC is bellow 5V, the output voltage threshold on PASS and FAIL will be less than 0.8*OPTO_VCC, which may not be identified by some controlling system.

## ATE workflow

When the system starts, it performs initialization until “XELTEK IS01” is shown on display screen. After that, it will be testing interface of USB, keyboard and ATE all the time. If signals of ATE SEL0-SEL5 aren’t all low, which means that ATE will select project, the system will enter ATE mode, that is, ATE work mode.

Note: When system enter offline mode, it will detect SD card first. If SD card is not found, it will prompt “NO SD FOUND!” User should insert SD card and restart system.

Create a project:

Create a project by SPIS01 software. Don’t forget to edit AUTO. After the project is generated, it can be downloaded into SD card by SPIS01 software or a card reader.

ATE workflow chart

Project Selection:

SEL0-SEL5 of IS01 ATE interface are used to select project. Using binary format, from 1 to 63, that means, user can select no more than 63 projects, e.g, SEL0 is high and the others are low, project 1 is selected; while both SEL0 and SEL1 are high, the others are low, project 3 is selected, etc.

Run algorithm:

After User selects the project, set pin START high, then the system starts programming.

# Text boxes

ATE Mode

1, Scan signal line of selecting projects

2, Show selected project name in the second row

3, Show “WAITING START” in the third row in LCD START…

Wait for Start signal…

Run algorithm, the light yellow

Operation result:

1, Light is green if success, while red if failed

2, LCD shows “AUTO OK” if success, while shows “AUTO FAIL” if failed

3, PASS of ATE interface is low if success while high if failed

Waiting for disconnect signal START…

Wait

Signal Start is high

Signal Start is low

Wait